## Slide 1: Infrared videography coupled with smart phone LED light for the measurement of pupil light reflex
Lily Y-L Chang 1, 3, 4, Jason Turuwhenua 1, 2, Tian Qu 1, Joanna Black 1, 3, 4, Monica L Acosta1, 3, 4
1 School of Optometry and Vision Science, Faculty of Medical and Health Sciences, The University of Auckland, New Zealand
2 Auckland Bioengineering Institute
3 Centre for Brain Research, The University of Auckland, New Zealand
4 New Zealand National Eye Centre, The University of Auckland, New Zealand
Notes: The overall purpose of this study is to validate and describe an IR videography set-up suitable for examination of the guinea pig pupil, which provides quantitative data on pupil diameter, and the extent of pupil constriction in response to light and re-dilatation.
Clinical assessment of the pupil appearance and pupillary light reflex informs us of the integrity of the autonomic nervous system, and is commonly assessed but only qualitatively, in optometric, ophthalmological and neurological clinics.

## Slide 2
I. Demonstration of experimental set-up (measurement of pupil diameter in human participants)

## Slide 3
Procedures involving human participants have been approved by the University of Auckland Human Participants Ethics Committee (reference number 010966).

## Slide 4
Filming of the measurement procedure: LC will measure subject’s pupil diameter by NeurOptics pupillometer, in one of the optometry research clinic rooms.
Notes: To validate the accuracy of our experimental set-up, firstly, the patient’s right pupil diameter is measured by the Neuroptics pupillometer (model: 59002, Neuroptics Inc, Irvine, CA, USA). The subject was dark adapted for 2 minutes prior to the measurement, and the results displayed on the Neuroptics pupillometer screen was recorded in a spreadsheet.

## Slide 5
Measurement of the horizontal visible iris diameter by slit lamp beam.
Filming: LC will examine subject’s horizontal visible iris diameter by slit lamp.
Notes:   Before beginning the measurement with IR pupillography, position the patient’s head in front of the slit lamp biomicroscope and measure the horizontal visible iris diameter of the R eye with the slit beam. Record the horizontal visible iris diameter in a spread sheet. Dark-adapt the subject for 2 minutes.

## Slide 6
Notes:   A firefly USB 2.0 infrared camera (Model #FMVU-03MTM-CS, 752x480 pixels, Point grey research, Canada) is attached to the eye piece of a slit lamp biomicroscope, with which the focus of the image can be adjusted by pushing the joystick back and forward.
  The patient is again positioned appropriately in front of a slit lamp biomicroscope and instructed to fixate on a red light on the wall approximately 6 m away.
  An infrared illumination system (5x 5 mm IR LEDs with peak spectral wavelength 940nm) is placed above the right eye to achieve high contrast filming conditions (Fig.1A).
  The right pupil is recorded for 10 seconds in audio visual interleave format using Point grey FlyCapture program at 30 frames per second (fps).

## Slide 7
Filming of the Macbook Pro screen as IR video is being recorded, followed by filming of the computer screen as The Matlab program analyses the video frame by frame.
Notes:   The known horizontal visible iris diameter measured previously is used to set the scale in our custom Matlab program as a reference for pupil diameter measurement.
  The centre of the pupil was marked with a white cross as a reference point to allow optimal detection of the pupil margin, and the corneal reflex was covered by a dark patch to avoid the program confusing the border of corneal reflex as pupil border.
The custom Matlab program outputs a spreadsheet with each frame number corresponding to a pupil diameter value. All measured values during the 10 s video are averaged to obtain the resting pupil diameter.

## Slide 8
II. Pupil light reflex measurement in guinea pigs

## Slide 9
Procedures involving animal subjects have been approved by the University of Auckland Animal Ethics Committee (reference number 001138).

## Slide 10
Notes:   The Right horizontal palpebral aperture (distance from temporal to nasal canthus) of the guinea pig is measured by a ruler.
  The guinea pig is gently held on an animal stage that allowed fine adjustment of lateral and vertical position.
  The guinea pig is left on the stage for 5 minutes to familiarize and adapt to the surrounding and the researchers, followed by a 2 minute dark adaptation period.

## Slide 11
Notes: The smart device strobe light stimulus (spectrum 405-780 nm white light, oval-shaped, 2x4.5mm) is set to have 0.2 second light ON - 5 seconds light OFF using the iStrobe LED Flash app (Work Avoidance Ltd). It is placed on the Left of the animal stage.
The guinea pig is gently held and placed on the animal stage so its Left eye is 5 cm away from the smart device white LED light stimulus, and its Right eye is in front of the IR camera.
The IR camera is controlled by a laptop computer, and records for 10 s before the first white LED light flash stimulates the Left pupil. From then on, the 0.2 second light ON - 5 seconds light OFF cycle is repeated 7 times.

## Slide 12
LC will add a video here that demonstrates how the custom Matlab program marks the centre of the pupil and pupil margin.
Notes: The known horizontal palpebral aperture distance measured previously is used to set the scale in our custom Matlab program as a reference for pupil diameter measurement.
The centre of the pupil was marked with a white cross as a reference point to allow optimal detection of the pupil margin, and the corneal reflex was covered by a dark patch to avoid the program confusing the border of corneal reflex as pupil border.
The custom Matlab program outputs a spreadsheet with each frame number corresponding to a pupil diameter value.

## Slide 13
III. Representative results

## Slide 14
Chart: Pupil Measurement
| A | B | C
Measurement by Neuroptic pupillometer | 7.1 | 7.7 | 6.9
Measurement by experimental set-up | 7.23 | 7.67 | 7.06
Notes: To determine whether using an IR illumination system results in comparable results to standard pupillometers, we obtained repeated measurements of the pupil diameter using the NeurOpticsTM pupillometer and compared the values with measurements obtained with the IR illumination system in three subjects. The results shown in figure 1D indicate that there are no significant differences with measurements from our experimental set-up

## Slide 15
Notes: This is a typical pupil diameter vs. frame number plot in a IR videography recording, showing (a.) pupil diameters at resting state (in black), (b.) negative pupil diameter change with light flash (in red), and (c.) positive pupil diameter change with cessation of light flash (in blue). Seven consecutive cycles are recorded for each video. The pupil light reflex was measured at 2 times points at 3 months and 7 months-old for both female males animals. Care was taken to include approximately equal numbers of males and females at both time points.

## Slide 16: Gender differences at juvenile age
 | Male | Female | Student’s t-test p-value
D1 (mm) | 7.42±0.22 | 5.43±0.32 | <0.05
CV (mm/s) | -2.02±0.18 | -1.13±0.10 | <0.01
AvCR (%) | 83.86±1.30 | 85.13±0.89 | >0.05
DV (mm/s) | 0.41±0.05 | 0.22±0.02 | <0.001
AvDR (%) | 95.81±0.72 | 98.54±0.31 | <0.001
Notes:   The following parameters are measured and calculated:
D1 = Resting pupil diameter = Average across resting period* (see Fig. 3a)
CV = Constriction velocity = Δ diameter/Δ time (see Fig. 3b)
AvCR = % constriction ratio = (Constricted pupil diameter/Resting pupil diameter) x 100
DV = Re-dilatation velocity = Δ diameter/Δ time (see Fig. 3c)
Av% re-dilatation ratio = (Re-dilated pupil diameter**/Resting pupil diameter***) x 100

## Slide 17: Gender differences at juvenile age
 | Male | Female | Student’s t-test p-value
D1 (mm) | 7.42±0.22 | 5.43±0.32 | <0.05
CV (mm/s) | -2.02±0.18 | -1.13±0.10 | <0.01
AvCR (%) | 83.86±1.30 | 85.13±0.89 | >0.05
DV (mm/s) | 0.41±0.05 | 0.22±0.02 | <0.001
AvDR (%) | 95.81±0.72 | 98.54±0.31 | <0.001
Notes:   The following parameters are measured and calculated:
D1 = Resting pupil diameter = Average across resting period* (see Fig. 3a)
CV = Constriction velocity = Δ diameter/Δ time (see Fig. 3b)
AvCR = % constriction ratio = (Constricted pupil diameter/Resting pupil diameter) x 100
DV = Re-dilatation velocity = Δ diameter/Δ time (see Fig. 3c)
AvDR = % re-dilatation ratio = (Re-dilated pupil diameter**/Resting pupil diameter***) x 100
At Juvenile age male guinea pigs had larger resting pupil size than female guinea pigs. In terms of PLR kinetics, juvenile male guinea pigs had greater constriction velocity and also quicker PLR recovery kinetics, with greater re-dilatation velocity. The juvenile male guinea pigs had both quicker pupil constriction and re-dilation velocity suggestive of a more readily mobile state of both the sphincter and dilator pupillae on stimulation of a PLR.

## Slide 18: Age specific effect in female guinea pigs
 | Juvenile Age (3-mths) | Adult Age (7-mths) | Student’s t-test p-value
D1 (mm) | 5.43±0.32 | 6.93±0.18 | <0.05
CV (mm/s) | -1.13±0.10 | -0.88±0.08 | <0.01
AvCR (%) | 85.13±0.89 | 88.65±0.77 | <0.001
DV (mm/s) | 0.22±0.02 | 0.17±0.01 | <0.05
AvDR (%) | 98.54±0.31 | 99.64±0.65 | >0.05
Notes: An age specific effect was detected in female guinea pigs when 3 months-old and 7 month-old data was compared. There were significant differences in all parameters between the female guinea pigs at 3 months and 7 months. Resting pupil size was larger in the adult female group than the juvenile female group. Constriction velocity was slower, and percentage constriction ratio was larger in the adult female group. This is suggestive of an age-related decline in parasympathetic input as the mobility of sphincter pupillae was acting more slowly, and constricted to a lesser extent in the adult animals, and that the sympathetic input to the dilator pupillae muscle was relatively more unopposed. Such age-related effect in pupil constriction parameters were not observed in male guinea pigs.

## Slide 19: Discussion
The quality of pupil measurement using this experimental set-up relies on even background illumination of the pupil with an IR LED array.
Care also must be taken to ensure that the stimulating white LED light from the smart device provides consistent and diffuse illumination of the pupil across all subjects.
Filming: One of the authors will say the following statements.

## Slide 20: Conclusion
The experimental set-up we have described is effective, accessible, and easy to assemble.
It allows measurement of pupil diameter and parameters of pupil mobility that were not previously possible in animal studies.
Such set-up for pupil assessment is useful for both research and clinical applications.
Filming: One of the authors will say the conclusion.

## Slide 21: 1,2,3,4University of Auckland
Lily Y-L Chang 1, 3, 4, Jason Turuwhenua 1, 2, Tian Qu 1, Joanna Black 1, 3, 4, Monica L Acosta1, 3, 4
1 School of Optometry and Vision Science, Faculty of Medical and Health Sciences
2 Auckland Bioengineering Institute
3 Centre for Brain Research
4 New Zealand National Eye Centre